## Slide 1: DETERMINATION OF WORKING LENGTH IN ENDODONTICS.

## Slide 2
1) INTRODUCTION.
2) SIGNIFICANCES OF WORKING LENGTH.
3) ANATOMICAL CONSIDERATIONS AND TERMINOLOGY.
4) USE OF REFERENCE POINTS.
5) HISTORICAL PERSPECTIVES.
6) METHODS OF DETERMINATION OF WORKING LENGTH.
A. RADIOGRAPHIC METHODS.
B. ELECTRONIC METHODS.
C. AUDIOMETRIC METHOD.
D. DIGITAL TACTILE SENSE METHOD.
E. PAPER POINT MEASUREMENT.
F. PATIENT RESPONSE.
7) CLINICAL SIGNIFICANCES.
8) SUMMARY AND CONCLUSION.
10) REFERENCES.

## Slide 3: THE SIGNIFICANCES OF WORKING LENGTH
The working length determines where the instruments are placed in canal and removal debris, metabolities, end products, & other unwanted items form the canal.
Limits the depth to which the canal filling is placed.
affects the degree of pain and discomfort that the patient feels following the appointment.
if calculated properly, it will play an important role in success of thetreatment

## Slide 4: ANATOMICAL CONSIDERATIONS AND TERMINOLOGY
WORKING LENGTH: - “The distance from a corona lreference point to the point at which canal preparation and obturation should terminate”. The ideal apical reference point in the canal is “apical stop”.
ANATOMIC APEX: - Is the tip (or) the end of the root determinedmorphologically.
RADIOGRAPHIC APEX: -Is the tip (or) the end of root determined radiographically.

## Slide 5
APICAL FORAMEN: - Is the region where the canal leaves the root surface next to the periodontal ligament. (American association of
Endodontists 1984),
it is the main apical opening of the root canal.
It is frequently eccentrically located away from the anatomic (or) radiographic apex.
Kuttler’s investigation showed 68 to 80% of teeth are deviated.
The anatomy of apical foramen changes with age.

## Slide 6
(a) The concept of the apex
(b)The apex of a younger person
(c) changing apex due to hard tissue deposition.

## Slide 7
ACCESSORY FORAMEN: - an orifice on the surface of the root communicating with a lateral (or) accessory canal.
may exist as a single foramen (or) as multiple foramina.

## Slide 8
APICAL CONSTRICTION: -
Minor diameter is the apical portion of theroot canal having the narrowest diameter.
The minor diameter widens apically to the foramen and assumes a funnel shape- Major diameter
funnel tapers to adistance short of the site of exiting and widens again. Because the adjacent walls of cementum are slightly convex (or) hyperbolic
when viewed in longitudinal section the configuration of the area between the major and minor diameter resembles that of a morning glory flower.
This configuration” is clearly visualized in an obturated radiograph when sealer is slightly extrudes past the apical constriction.

## Slide 9
Dummer et, al (1984) classified the apical constriction into 4 types
A: minor diameter
B: major diameter

## Slide 10: CEMENTODENTINAL JUNCTION
region where the dentin and cementum are united point at which the cemental surface terminates at (or) near the apex of a tooth.
CDJ histological landmark,cannot be located radio graphically (or) clinically.
Langeland  CDJ does not always coincide with the apical
constriction. Located 0.5 to 3.0mm short of the anatomic apex.
The apical constriction is located 0.5 to 1.0mm short of the radiographic apex
Due to variations; the problem exists in locating apical landmarks and in interpreting their positions on radiographs.

## Slide 11: REFERENCE POINTS
Anterior teeth  Incisal edge
Premolars 2 canals buccal canal buccal cusp
Molars  crossing of files
    Upper molar mesio buccal disto palatal
    disto-buccal mesio palatal
    palatal  buccal groove
    Lower molar mesio-buccal mesio-lingual
    ML mesio-buccal
    distal mesial MR

## Slide 12: Stop attachments
metal, silicone rubber and plastic
AvailableTear drop silicone –advantage  positioned to indicate canal curvature
do not have to be removed form the instrument during sterilization at 450 F
should be perpendicular and not oblique to the shaft of the instrument
Length adjustments against the edge of a sterile metric ruler or endo- guaze
disadvantages like movement of up (or) down the shaft, leading toshort (or) past the apical constriction

## Slide 13: HISTORICAL PERSPECTIVES
19th century no radiograph pt. response used led to multiple errors
Kells in 1899introduced radiograph to dentistry error due to miscalculations
1900’s
1920’s -Grove concluded that pulp tissue could not extend beyond the CDJ because the cell unique to the dental pulp, the odontoblast, was not found past the CDJ.
Hatton and grove – advised that preparation beyond the CDJ would result in injury to periapical tissue.
Blayney and Coolidge – Histological evaluations indicating that filling short of the root tip gave the best results.

## Slide 14
In 1955 Kuttler - Studied the microscopic anatomy of root tip, and decided that filing to the radiographic apex was an unwise clinical procedure
contributing to post operative pain and lowering the production of successful cases.
many decided to file specific distances away from the root tip in an effort to stop filing into the periapical tissues.
Some aspects of Kuttler’s study have been questioned. The teeth that he
studied had no caries, either no restorations or no periapical lesions  that are not often treated endodontically.

## Slide 15
THE MOST COMMON METHODS ARE.
  i. RADIOGRAPHIC METHODS.
  ii. ELECTRONIC METHODS.
  iii. AUDIOMETRIC METHOD.
  iv. DIGITAL TACTILE SENSE METHOD.
  v. PAPER POINT MEASUREMENT.
  vi. PATIENT RESPONSE.

## Slide 16
  RADIOGRAPHIC METHODS ARE
  GROSSMAN‘s method.
  INGLE‘s technique.
  WEINE’s modification.
  CURVED canals.
  OTHER METHODS,
  BEST METHOD.
  BREGMEN METHOD.
  BRAMANTE METHOD.
  EVERETT AND FIXOT GRID SYSTEM.
  EUCLIDEAN ENDOMETRY.
  RECENT ADVANCES IN RADIOGRAPHIC METHODS,
  RADIOVISIO GRAPHY. (RVG)
  XERORADIO GRAPHY.
  DIGITAL IMAGE PROCESSING.
  LASER OPTICAL DISK STORAGE.

## Slide 17: RADIOGRAPHIC METHODS
Grossman’s method
instrument extending to the apical constriction is  by digital tactile sense and a radiograph is taken.
A mark (or) stopper is placed at the occlusal (or) incisal
reference point which will also be detectable on the radiograph.
By measuring the length of radiographic images of both the tooth and measuring instrument as well as the actual length of the instrument the clinician can determine the actual length of the tooth by a mathematical formula.

## Slide 18
INGLE’S TECHNIQUE:-
1.Good, undistorted, preoperative radiographs
2. Adequate coronal access to all canals.
3. An endodontic millimeter ruler.
4. Working knowledge of the average length of all of the teeth.
5. A definite, repeatable plane of references / anatomic landmark on the tooth, should be noted on the patient’s record.

## Slide 20
Clarks rule (SLOB technique)

## Slide 21: Weine’s modification
1. If no root (or) bone resorption is evident preparation should terminate1.0mm from the apical foramen.
2. If bone resorption is apparent but there is no root resorption shorten the length by 1.5mm
3. If both root and bone resorption is apparent shorten the length by 2.0mm.

## Slide 22
BEST METHOD:as described by Best: A 10mm steel pin was fixed to the labial surface of the tooth with utility wax in a position parallel to its long axis before radiograph obtained.
The radiograph so obtained was carried to the BW gauge which indicates the tooth length.
Best attained little success, generally resulting in lengths greater than thereal length of the teeth.

## Slide 23
BREGMAN METHOD
In this method flat probes, 25mm. in length, were prepared.
Each had a steel blade fixed with acrylic resin as a stop, leaving a free segment of 10mm for placement into the root canal.
This probe was placed in the tooth until the metallic end touched the incisal edge (or) cusp tip of the tooth.
Then a radiograph was taken.
In the radiographic image the following factors were measured:

## Slide 24
CAD = Apparent tooth length, seen in the radiograph.
CRI = Real instrument length.
CAI = Apparent instrument length, seen in the radiograph.

## Slide 25
BRAMANTE METHOD
Bramante,(1970)

## Slide 26
GRID SYSTEM:
Everett and Fixot (1963) The diagnostic x-ray designed
Enameled copper wire is placed into Plexiglas and fixed to regular periapical film.
The grid is taped to the film to lie between the tooth and film during exposure so that the pattern becomes incorporated in the finished film.

## Slide 27
Disadvantages of radiographic methods
1. Anatomic structures and radiopaque materials may be super imposed on the image of the root.
2. The biologic risk of radiation.
3. The procedure is time consuming.
4. Radiograph is a two dimensional representation of a three dimensional object.
5. The apical foramen could not be correctly identified because it frequently deviated from the anatomic apex.
6. Patient with gag reflex (or) limited mouth opening may inhibit takingradiographs

## Slide 28
Recent advances in radographic techniques
        1.RADIO VISIO GRAPHY. (RVG)
        2. XERORADIO GRAPHY.
        3. DIGITAL IMAGE PROCESSING.
        4. LASER OPTICAL DISK STORAGE.

## Slide 29: Radio visual graphy
Introduced by Francis Mouyen
Disadv of silver halide films
    1. Fairly high radiation dose is needed.
    2. Film processing interrupts treatment.
Components- The Radio
-The Visual
-The Graphy

## Slide 30
Advantages
-no special technique required
-low radiation dosage
-no film processing
-contrast adjustments can be done
-Teletransmission
Disadvantages
  Expensive

## Slide 31: Xeroradiography
Chester F. Carlson in 1937
use of an aluminum plate that is coated with a layer of vitreous selenium
The selenium particles are given a uniform electrostatic charge. The charged plate is placed in a light proof, airtight cassette.
When the film is exposed, it causes a selective discharge of the selenium depending upon the amount of radiation used and relative density of the object.

## Slide 32
Xeroradiographic image differ from conventional radiograph.
1) It exhibits high edge contrast due to phenomenon called edge enhancement. This facilitates perception of anatomic details.
2) The image is on paper and is viewed in reflected light.
3) Choice of positive and negative image is possible
Advantages of Xeroradiography are.
1 Reduction in exposure time.
2 Ease in manipulation.
3 Ease of viewing.
4 Edge enhancement. (Boundary between structures is clear).

## Slide 33: LASER OPTICAL DISK STORAGE
Laser optical disks are a useful medium to store radiographic images.
The image is recorded by a focused laser beam heating a thin film of tellurium sub oxide at specific points on the optical disk to a higher reflective value
The recovery of image from the optical disk is accomplished by the detection of reflected light from the disk surface at the points with the higher reflective value
When compared with normal radiographs, this method has been shown to produce images that are equal to and in some circumstances of superior diagnostic merit.

## Slide 34
HISTORY
In 1918, CUSTER was the first to report the use of electric current to determine working length
In 1942, SUZUKI, reported his study on iontophoresis of ammoniated silver nitrate in the teeth of dogs was that the electrical resistance between the root canal instrument inserted into a root canal and an electrode applied to the oral mucous membrane registered a consistent valueof approximately 6.5 kilo ohms (kW).

## Slide 35
In 1960 GORDON, was the second to report the use of clinical device for electrical measurement of root canals.
In 1962 SUNADA, adopted the principle of Suzuki and was the first to describe the detail of a simple device to measure working length with a constant resistance of 6.5 (kw)
In 1987, HUANG, reported that this principle is not a biologic characteristic, but rather a physical principles of electricity alone.

## Slide 36: DETERMINATION OF WORKING LENGTH BY ELECTRONICS
1. HISTORY
2. BASIC FUNCTION OF ELECTRONIC APEX LOCATORS(EAL)
3. CLASSIFICATIONS OF ELECTRONIC APEX LOCATORS

## Slide 37
CLASSIFICATIONS OF ELECTRONIC APEX LOCATORS ( Mc Donald).
FIRST GENERATION.
1st Generation apex locators, also known as RESISTANCE apex locators.
Principles: measures opposition to the flow of direct current (or) resistance.
When the file of the reamer reaches the apex in the canal, the resistance value is 6.5 kW (current 40ma).

## Slide 38
The root canal meter(1969) –
150 HZ current is used.
Pain was often due to high current.
Endodontic meter and Endodontic meter S II
which used a current of less than 5μA.
Inoue audiometric component apex locators in 1970’s & 80’s  “Sono- Explorer”
1975 Neosono have improved circuitry, are more compacted and are easy to operate .
1st generation are Dentometer and Endo Radar

## Slide 39
DISADVANTAGES:
Readings longer (or) shorter than the accepted working length.
The resistance type EAL’S yield inaccurate results
-electrolytes,
-excessive moisture,
-vital pulp tissue,
-exudates
-excessive hemorrhage

## Slide 40
SECOND GENERATION (IMPEDANCE apex locators)
Principle: Measures opposition to the flow of alternating current (or) impedance.
DEFINITION of IMPEDANCE: An apparent increase of resistance to an alternating current owing to induction in a circuit.

## Slide 41
Inoue in 1971 as “Sono –Explorer is calibrated at the periodontal pocket of each tooth and measured by the feedback of the oscillator loop.
The beeping of the device indicated when the apex was reached.
A later model, the Sonoexplorer MK III uses a meter to indicate distance to apex.
This device operates on a current of single low frequency.

## Slide 42
Endocator
can be used in presence of electro conductive fluids.
Here a high frequency(400 KHZ) current used.
With an electrode connected to the dental chair and a Teflon sheath over the probe was able to make measurements in canals even with conductive fluids
The Teflon sheath coated filewas difficult use in narrow canals and was affected by autoclaving.
Patient was uncomfortable due to high current used.

## Slide 43
THE APEX FINDER: -
-Has a visual digital LED indicator and pulptester.
THE ENDO ANALYZER:
- Is a combined apex locator and pulp tester.
DIGIPEX:-
-Has a visual LED digital indicator and an audible indicator. It requires calibration.
DIGIPEX II:
-Is a combination of apex locator and pulp tester

## Slide 44
EXACT – A – PEX: -
-Has an LED bar graph display and audio indicator.
FORMATRON:-
-Has a flashing LED light and a digital LED display and
-does not require calibration.
-This device is small, light weight and inexpensive.
THE PIO: -
  Apex locator has an analog meter display and an audioindicator.
  It has an adjusting knob for calibration.

## Slide 45
DISADVANTAGES:-
Root canal has to be reasonably free of electro conductive materials
This created a “catch- 22”
not all apex locators incorporated the same degree of sophistication in electronic circuitry
sensitivity to compensate for the intra canal environment (or) indicates on its display that it should be switched from a wet to a dry made (or) viceversa.

## Slide 46
THE THIRD GENERATION (OR) FREQUENCY DEPENDENT
principle: the reactive component facilitates the flow of alternating current, more for higher than for lower frequencies.
Thus a tissue through which two alternating currents of different frequencies are flowing will impede the lower frequency current more than the higher frequency current.
The reactive component of the circuit may changes in a canal. When this occurs, the impedances offered by the circuit to currents of differing frequencies will change relative to each other.

## Slide 47
1. ENDEX: (or) APIT –Yamaoka et al.
very low alternating current. two frequencies (5 &1 KHZ)
. As the attached endodontic reamer enters the coronal part of the canal, the difference in the
impedances at the two frequencies is small.
As the instrument is advanced apically, the difference in impedance values begins to change.
As the apical constriction is reached, the impedance values are at their maximum
these difference are indicated on the analog meter and audio
alarm. This impedance difference is the basis of the “difference method”.
The unit must then be reset for each canal.

## Slide 48
The major advantage
works well regardless of the presence of pus (or) electroconductive environments in the canal.
However a disadvantage is that a calibration needs to be done each time.

## Slide 49
The APEX FINDER. A.F.A (All fluids allowed).
frequency dependent EAL, which uses five different frequencies (0.5, 1,2,4,8 KHZ) & to read four amplitude ratio’s.
The unit is self – calibrating and can measure with electrolyte present in the canal.

## Slide 50
NEOSONO ULTIMA – EZ Apex locators.
MARK V PLUS
JUSTWO (or) JUSTY II

## Slide 51
ROOT ZX:-
A third generation apex locator that uses dual frequency and comparative impedance principles (Kobayashi).
was the ratio method (or) division method.
The Root ZXmeasures the two impedances at two frequencies (8 and 0.4 KHZ) inside the canal
A micro processor in the device calculates the ratio of the two frequencies.
The quotient of the impedance is displayed on an LCD (Liquid Crystal Display) meter panel and represents the position of the Instrument inside the canal.
The Root ZX is mainly based on detecting the change in electrical capacitance that occurs near the apical constriction.

## Slide 52
Advantages
- It requires no adjustment (or) calibration
- Can be used when the canal is filled with strong electrolyte (or) when the canal is “empty” and moist
-The meter is an easy to read LCD

## Slide 53
PROPEX:-
Is a modern apex locator based on multi frequency
enables to locate apicalforamen with great precision in any canal condition.
Propex screen facilitates the access to the exact file position.
Propex audio signals combined with the screen information helps about 2-3mm before the apex is reached.
Propex warns when the file approaching the apical zone by emitting 2 beeps

## Slide 54
FORMATRON D-10. ( Parkell company)
Monitors the impedance between the lip clip and the file,
being sensitive to both the voltage applied and the current
circuit with current of multiple frequencies.
The D-10 does not feature an LCD
adorned by a string of colored lights
When for short of foramen,  Green.
Cautionary yellow  approaches close to the foramen.
Red light  apical foramen.
orange light beyond apex and device starts beeping.

## Slide 55
FOURTH GENERATION:-
The BINGO 1020 / RAY – PEX 4\5. (Forum engineering technologies Israel).
two separate frequencies 400 HZ and 8 KHZ similar to the 3rd generation units.
claim that the combination of using only one frequency at a time and basing measurements on the root mean square values of the signals increases the measurement accuracy and the reliability of the device.
An in vitro study found Bingo 1020 is as reliable as the Root ZX and user friendly
marketed by Dentsply as RAY - PEX 4.

## Slide 56
Bingo 1020
Raypex5

## Slide 57: APEX LOCATOR & ENDONTIC HANDPIECE
Tri Auto ZX: Root ZX apex locator+ hand piece uses NI-TI rotary instruments that rotates at 280 ± 50rpm.
rotary instrument is monitored on the LED control panel of the handpiece during the shaping and cleaning of the canal.
Tri auto ZX has three automatic safety mechanisms.
-Auto start-stop mechanism
-Auto torque reverse mechanism
-Auto – apical – reverse mechanism

## Slide 58
Tri Auto ZX has four modes
-Electrical measurement of root (EMR) mode
-The low mode
-High mode
-MANUAL MODE

## Slide 59: ELEMENT DIAGNOSTIC UNIT & APEX LOCATOR
device does not process the impedance information as a mathematical algorithm,  takes the resistance and capacitance measurements and compares  database to determine the working length
uses a composite waveform of two signals0.5 and 4 KHZ.

## Slide 60
signals go through a digital – to - analogue converter to be converted into an analogue signal
The feedback signal wave forms are then fed into a noise reduction circuit.
The manufacturer claims that this allows less sampling error per measurement and more consistent readings.

## Slide 61
ADVANTAGES OF THE ELECTRONIC METHOD.
1. Only method that can measure length up to apical foramen, not to
radiographic apex..
2. Accurate
3. Easy and fast
4. Reduction of X-ray exposures
5. Artificial perforation can be recognized.

## Slide 62
DISADVANTAGES OF THE ELECTRONIC METHOD.
1. Requires special device
2. Accuracy is influenced by electrical condition of canal
3. Difficult in teeth with wide open apex.
4. Inconsistent results in cases of vital teeth (except newly developed
devices).

## Slide 63
HOW THE APEX LOCATORS SHOULD BE USED?
General Instructions: In electronic measurements a stable circuit should be build between the measured canal and the device.
Electrical connection: At each electric contact point (File holder – file, Lip clip mucous membrane) a firm electric connection is required.
Cervical leakage: The cervical leakage of the measuring current is the greatest cause of the inaccurate measurements (high reading) in the electronic method.
The causes of cervical leakage might be metal restorations, decay of the teeth, and electro conductive irrigants.

## Slide 64
Dry canals:-low readings (obtaining long working length) can occur with extremely dry canals in the measurement involving conventional apex locators.
Long Root:-It is reported that high readings (obtained a short working length) occurred in teeth with extremely long roots in the measurement involving conventional apex locators.
Lateral canal:-If the tooth has a large lateral canal, the meter may indicate the apex in an early stage of the measurement when the file tip reaches aninner opening of the lateral canal.
Open apex: - If the tooth has a wide open apex, the electronic measurement is almost impossible. The radiographic method is recommended.

## Slide 65
Other uses of apex EAL’s
used to detect root perforations and pulpal floor perforations.
aids in diagnosis of external resorption that had invaded the dental pulp space or internal resorption that had perforated to the external root surface.
pin holes can be checked to detect perforations into pulp or periodontal ligament.
Horizontal or vertical root fractures could also be detected as well as post perforations.

## Slide 66
Accuracy in primary teeth:
The location of the apical foramen in the primary teeth, physiologic root resorption,  challenge
Katz et al  Root ZX had an accuracy that was similar to actual length and the radiograph film and with a tendency of slightly underestimate the root canal length by 0.98 mm of the apex.
The tooth, root canal type, status of the periapex and clinical conditions did not influence these results.

## Slide 67
Effect of foramen size on the accuracy of EAL:
there is a consensus that the file size does not affect the accuracy of EAL’s
Nguyen et al, effect on the measurement of the relative diameters of the file and root canal using Root ZX. The initial canal length was measured by using EAL
was enlarged to size 60 and length determined with no 10 and no 60 file.
The position of the file tip was observed histomorphometrically after the apical 4mm of the canal was exposed by grinding the buccal aspect of the root.
Differences the final length 10 to 60 and initial lengths were similar.

## Slide 68
Effect of resorption on the accuracy of EAL’s:
The use of EAL’s in apical resorption is under question  possible destruction of the apical constricture and the loss of periodontal tissue.
Goldberg et al, reported that the accuracy of EAL in apical resorption may depend on the operators experience and could locate root end consistently even with the resorption lacunae.

## Slide 69
Effect of different metal Types:
Nekoofar et al,evaluated the accuracy of Neosono ultima EZ with nickel titanium and stainless steel files
accuracy of Ni - ti is 94% and stainless files is 92%
there was no statistically significant difference
Contraindications pt. with cardiac cardiac pacemaker

## Slide 70
Conventional radiograph still is needed?
Yes. The EAL’s only provide the electronic impedance and not the canal shape. To obtain anatomic information of the roots and canals, Medico
legal record keeping requirements a radiograph is still mandatory in an endodontic procedure.

## Slide 71: Common problems
Unstable electronic signal with rapid wandering signs. frequently when the file touches the metallic restorations (or) cervical leak through the sub gingival caries.
Sharp drop of the signal at the apical foramen. When the file tip is at the extremely dried point, there is little (or) no electric current, even at higher frequencies. As soon as it meets with the apical tissue, a sudden circuit breaks out, which brings the signal to the apex mark.

## Slide 72
Apex sign from the beginning severely bleeding (or) exudating canal.At times, the signal reaches the APEX mark before the file enters the foramen area.  due to electrolyte in the canal. This phenomenon occurs often with extreme bleeding and actively draining pus from the canal.
Premature reading, open apexWhen there is open (or) blunderbuss – type foramen, the meter tends to read short from the true apical foramen.
Premature reading is probably due to sharp drop in the gradient of the impedance ratio at the thin dentin walls.

## Slide 73
AUDIOMETRIC METHOD(Inoue in 1985).
a variation on the principal of electrical resistance of comparative tissue
uses low frequency oscillation sound to indicate when similarity to electric resistance has occurred by a similar sound response.
By placing an instrument in the gingival sulcus and inducing an electric current until sound is produced, and then repeating this by placing an instrument through the root canal until the same sound is heard
determine working length determines working length.

## Slide 74
DIGITAL TACTILE SENSE.
possible to gauge the apical constriction of the root canal system by tactile sense.
several problems with this method
not all the teeth possess an apical constriction
ability to gauge the apical constriction relies on the presence of a natural canal taper that has a minimal constriction only at the termination of the canal.
relies upon the selection of a file size that will first bind only at the apical constriction,
It is ineffective in root canals with an immature apex
highly inaccurate if the canal is constricted through out its entire length.
supplementary to high quality, carefully aligned, parallel, working length radiographs and apex locator.

## Slide 75
PAPER POINTS
immature apexthe most reliable means of determining working length
gently pass the blunt end of a paper point into the canal after profound anesthesia
The moisture (or) blood on the portion of the paper point may be an estimation of working length (or) the junction between the root apex and the bone.
paper point measurement method is a supplementary one.
A new dimension has recently been added to paper points by the addition of markings. at 18, 19, 20, 22 and 24 mm
These paper points were designed to ensure that they be inserted fully to the apical constriction.
The accuracy of these markings should be checked on a millimeter ruler.

## Slide 76
PATIENT RESPONSE

## Slide 77
CLINICAL SIGNIFICANCES
Before determining working length the coronal access to the pulp chamber should be in a straight line with easy path of insertion and removal of endodontic instruments
It is very important to monitor the working length periodically sincethe working length may change as a carved canal is straightened.
Optimal length of canal preparation and the optimal level of canal obturation end point is the apical constrictionto improve the apical seal when the canal is obturated.

## Slide 78
Failure to determine working length and maintaining over or under instrumentation  lead to perforation through the apical constriction.
Destruction of the constriction may lead increased incidence of postoperative pain, prolonged healing period, incomplete regeneration of cementum, PDL and alveolar bone.

## Slide 79
Failures to determine and maintain working length lead to shaping and cleaning short of the apical constriction  Leading to persistent discomfort, incomplete apical seal, apical leakage, supports the continued existence of viable bacteria and contributes to a continued periradicular lesion and lowers the rate of success.
In this era of improved illumination and magnification, working
length determination should be to the nearest one – half millimeter.

## Slide 80
Conclusion

## Slide 81
REFERENCES
1) FRANKLIN.I. WEINE. – Endodontic therapy. 6th edition
2) GROSSMAN- Endodontic practice. 11th edition.
3) JOHN. I. INGLE. – Endodontics. 5th edition.
4) PARAMESWARAN- Current trends in endodontology.
5) STOCK. – Atlas of endodontics. 3 rd edition..
6) ALEXANDER et. al,Tooth Length determination: A review;“000” 1991:72:238 242.
7) BRAMANTE & BERBERT et al, A critical evaluation of some methods of determining tooth length. 000. 1974; 37; 463-473.
8) FRANCIS MOUYEN. et al,Presentation and physical evaluation of R.V.G. 000; 1989; 68; 238-242.
9) GORDON et al, Review of electronic apex locator. I.E.J; 2004; 37, 425-437.
10) KAUFMAAN et al, Determination of location of root perforations by EAL’s000; 1996; 82: 324-329.